SAFETY DATA SHEET

# Identification

## Product identifier FAS-MARK Cover Paint

Other means of identification FM150, FM15Y, FM15BR, FM15R, FM15G, FM15BL, FM15P. FM15W, FM15B, FM 15BRZ

Company name	FEDERAL PROCESS CORPORATION

## ADDRESS

Emergency phone number

4520 Richmond Road

Cleveland, Ohio 44128

Chemtrec Phone

800-424-9300

# Hazard(s) identification

## Physical hazards Health hazards

Environmental hazards

OSHA defined hazards Label elements

Flammable aerosols Gases under pressure

Serious eye damage/eye irritation Carcinogenicity

Reproductive toxicity

Specific target organ toxicity, single exposure

Specific target organ toxicity, repeated exposure

Hazardous to the aquatic environment, acute hazard

Hazardous to the aquatic environment, long-term hazard

Not classified.

Category 1 Liquefied gas Category 2A Category 1A Category 2

Category 3 narcotic effects Category 1

Category 2

Category 3

Signal word	Danger

Hazard statement	Extremely flammable aerosol. Contains gas under pressure; may explode if heated. Causes serious eye irritation. May cause drowsiness or dizziness. May cause cancer. Suspected of damaging fertility or the unborn child. Causes damage to organs through prolonged or repeated exposure. Toxic to aquatic life. Harmful to aquatic life with long lasting effects.

## Precautionary statement

Prevention	Obtain special instructions before use. Do not handle until all safety precautions have been read and understood. Keep away from heat/sparks/open flames/hot surfaces. - No smoking. Do not spray on an open flame or other ignition source. Pressurized container: Do not pierce or burn, even after use. Do not breathe mist or vapor. Wash thoroughly after handling. Do not eat, drink or smoke when using this product. Use only outdoors or in a well-ventilated area. Avoid release to the environment. Wear protective gloves/protective clothing/eye protection/face protection.

Response	If inhaled: Remove person to fresh air and keep comfortable for breathing. If in eyes: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. If exposed or concerned: Get medical advice/attention. Call a poison center/doctor if you feel unwell. If eye irritation persists: Get medical advice/attention.

Material name: FAS-MARK Cover Paint

Storage	Store in a well-ventilated place. Keep container tightly closed. Store locked up. Protect from sunlight. Store in a well-ventilated place. Protect from sunlight. Do not expose to temperatures exceeding 50°C/122°F.

Disposal	Dispose of contents/container in accordance with local/regional/national/international regulations.

## Hazard(s) not otherwise classified (HNOC)

None known.

Supplemental information	55.82% of the mixture consists of component(s) of unknown acute hazards to the aquatic environment. 55.82% of the mixture consists of component(s) of unknown long-term hazards to the aquatic environment.

# Composition/information on ingredients

## Mixtures

Chemical name

Common name and synonyms

CAS number	%

ACETONE N-BUTANE PROPANE

BARIUM SULFATE TITANIUM DIOXIDE 2-PENTANONE

PROPYLENE GLYCOL METHYL ETHER ACETATE

TALC XYLENE

ETHYLBENZENE

SILICA, CRYSTALLINE QUARTZ

67-64-1

106-97-8

74-98-6

7727-43-7

13463-67-7

107-87-9

108-65-6

14807-96-6

1330-20-7

100-41-4

14808-60-7

30 to <40

10 to <20

10 to <20

5 to <10

5 to <10

1 to <5

1 to <5

1 to <5

1 to <5

0.1 to <1

0.1 to <1

Other components below reportable levels	10 to <20

*Designates that a specific chemical identity and/or percentage of composition has been withheld as a trade secret.

# First-aid measures

Inhalation	Remove victim to fresh air and keep at rest in a position comfortable for breathing. Call a POISON CENTER or doctor/physician if you feel unwell.

Skin contact	No adverse effects due to skin contact are expected. Wash off with soap and water. Get medical attention if irritation develops and persists.

Eye contact	Immediately flush eyes with plenty of water for at least 15 minutes. Remove contact lenses, if present and easy to do. Continue rinsing. If eye irritation persists: Get medical advice/attention. No specific first aid measures noted.

Ingestion	Not likely, due to the form of the product. In the unlikely event of swallowing contact a physician or poison control center. Rinse mouth.

## Most important symptoms/effects, acute and delayed

Indication of immediate medical attention and special treatment needed

May cause drowsiness and dizziness. Headache. Nausea, vomiting. Severe eye irritation. Symptoms may include stinging, tearing, redness, swelling, and blurred vision. Prolonged exposure may cause chronic effects.

Provide general supportive measures and treat symptomatically. Keep victim under observation. Symptoms may be delayed.

General information	IF exposed or concerned: Get medical advice/attention. If you feel unwell, seek medical advice (show the label where possible). Ensure that medical personnel are aware of the material(s) involved, and take precautions to protect themselves. Show this safety data sheet to the doctor in attendance.

# Fire-fighting measures

Suitable extinguishing media	Alcohol resistant foam. Water fog. Dry chemical powder. Carbon dioxide (CO2).

## Unsuitable extinguishing media

Specific hazards arising from the chemical

Special protective equipment and precautions for firefighters

Do not use water jet as an extinguisher, as this will spread the fire.

Contents under pressure. Pressurized container may explode when exposed to heat or flame. During fire, gases hazardous to health may be formed.

Firefighters must use standard protective equipment including flame retardant coat, helmet with face shield, gloves, rubber boots, and in enclosed spaces, SCBA.

## Fire fighting equipment/instructions

In case of fire: Stop leak if safe to do so. Do not move cargo or vehicle if cargo has been exposed to heat. Move containers from fire area if you can do so without risk. Containers should be cooled with water to prevent vapor pressure build up. For massive fire in cargo area, use unmanned hose holder or monitor nozzles, if possible. If not, withdraw and let fire burn out.

Specific methods	Use standard firefighting procedures and consider the hazards of other involved materials. Move containers from fire area if you can do so without risk. In the event of fire and/or explosion do not breathe fumes.

General fire hazards	Extremely flammable aerosol. Contents under pressure. Pressurized container may explode when exposed to heat or flame.

# Accidental release measures

## Personal precautions, protective equipment and emergency procedures

Methods and materials for containment and cleaning up

Keep unnecessary personnel away. Keep people away from and upwind of spill/leak. Keep out of low areas. Many gases are heavier than air and will spread along ground and collect in low or confined areas (sewers, basements, tanks). Wear appropriate protective equipment and clothing during clean-up. Do not breathe mist or vapor. Emergency personnel need self-contained breathing equipment. Do not touch damaged containers or spilled material unless wearing appropriate protective clothing. Ventilate closed spaces before entering them. Local authorities should be advised if significant spillages cannot be contained. For personal protection, see section 8 of the SDS.

Refer to attached safety data sheets and/or instructions for use. Eliminate all ignition sources (no smoking, flares, sparks, or flames in immediate area). Keep combustibles (wood, paper, oil, etc.) away from spilled material. Stop leak if you can do so without risk. Move the cylinder to a safe and open area if the leak is irreparable. Isolate area until gas has dispersed. Cover with plastic sheet to prevent spreading. Absorb in vermiculite, dry sand or earth and place into containers. Prevent product from entering drains. Following product recovery, flush area with water.

Small Spills: Wipe up with absorbent material (e.g. cloth, fleece). Clean surface thoroughly to remove residual contamination. For waste disposal, see section 13 of the SDS.

Environmental precautions	Avoid release to the environment. Prevent further leakage or spillage if safe to do so. Avoid discharge into drains, water courses or onto the ground. Inform appropriate managerial or supervisory personnel of all environmental releases.

# Handling and storage

Precautions for safe handling	Obtain special instructions before use. Do not handle until all safety precautions have been read and understood. Pressurized container: Do not pierce or burn, even after use. Do not use if spray button is missing or defective. Do not spray on a naked flame or any other incandescent material. Do not smoke while using or until sprayed surface is thoroughly dry. Do not cut, weld, solder, drill, grind, or expose containers to heat, flame, sparks, or other sources of ignition. All equipment used when handling the product must be grounded. Do not re-use empty containers. Do not breathe  mist or vapor. Avoid contact with eyes. Avoid prolonged exposure. When using, do not eat, drink or smoke. Pregnant or breastfeeding women must not handle this product. Should be handled in closed systems, if possible. Use only in well-ventilated areas. Wear appropriate personal   protective equipment. Wash hands thoroughly after handling. Avoid release to the environment.

Observe good industrial hygiene practices.

## Conditions for safe storage, including any incompatibilities

Level 2 Aerosol.

Store locked up. Pressurized container. Protect from sunlight and do not expose to temperatures exceeding 50°C/122 °F. Do not puncture, incinerate or crush. Do not handle or store near an open flame, heat or other sources of ignition. This material can accumulate static charge which may cause spark and become an ignition source. Secure cylinders in an upright position at all times, close all valves when not in use. Store in a well-ventilated place. Store away from incompatible materials (see Section 10 of the SDS).

# Exposure controls/personal protection

## Occupational exposure limits

US. OSHA Table Z-1 Limits for Air Contaminants (29 CFR 1910.1000)

Components

Type

Value

Form

2-PENTANONE (CAS

107-87-9)

ACETONE (CAS 67-64-1)

BARIUM SULFATE (CAS 7727-43-7)

PEL	700 mg/m3

200 ppm

PEL	2400 mg/m3

1000 ppm

PEL	5 mg/m3	Respirable fraction.

15 mg/m3	Total dust.

## US. OSHA Table Z-1 Limits for Air Contaminants (29 CFR 1910.1000)

| Components | Type | Value | Form |
| --- | --- | --- | --- |
| ETHYLBENZENE (CAS 100-41-4) | PEL | 435 mg/m3 |  |
|  |  | 100 ppm |  |
| PROPANE (CAS 74-98-6) | PEL | 1800 mg/m3 |  |
|  |  | 1000 ppm |  |
| TITANIUM DIOXIDE (CAS 13463-67-7) | PEL | 15 mg/m3 | Total dust. |
| XYLENE (CAS 1330-20-7) | PEL | 435 mg/m3 |  |
|  |  | 100 ppm |  |
| US. OSHA Table Z-3 (29 CFR 1910.1000) |  |  |  |
| Components | Type | Value | Form |
| SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7) | TWA | 0.3 mg/m3 | Total dust. |
|  |  | 0.1 mg/m3 | Respirable. |
|  |  | 2.4 mppcf | Respirable. |
| TALC (CAS 14807-96-6) | TWA | 0.3 mg/m3 | Total dust. |
|  |  | 0.1 mg/m3 | Respirable. |
|  |  | 20 mppcf |  |
|  |  | 2.4 mppcf | Respirable. |
| US. ACGIH Threshold Limit Values |  |  |  |
| Components | Type | Value | Form |
| 2-PENTANONE (CAS 107-87-9) | STEL | 150 ppm |  |
| ACETONE (CAS 67-64-1) | STEL | 750 ppm |  |
|  | TWA | 500 ppm |  |
| BARIUM SULFATE (CAS 7727-43-7) | TWA | 5 mg/m3 | Inhalable fraction. |
| ETHYLBENZENE (CAS 100-41-4) | TWA | 20 ppm |  |
| N-BUTANE (CAS 106-97-8) | STEL | 1000 ppm |  |
| SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7) | TWA | 0.025 mg/m3 | Respirable fraction. |
| TALC (CAS 14807-96-6) | TWA | 2 mg/m3 | Respirable fraction. |
| TITANIUM DIOXIDE (CAS 13463-67-7) | TWA | 10 mg/m3 |  |
| XYLENE (CAS 1330-20-7) | STEL | 150 ppm |  |
|  | TWA | 100 ppm |  |

US. NIOSH: Pocket Guide to Chemical Hazards

Components

Type

Value

Form

2-PENTANONE (CAS

107-87-9)

ACETONE (CAS 67-64-1)

BARIUM SULFATE (CAS 7727-43-7)

ETHYLBENZENE (CAS 100-41-4)

N-BUTANE (CAS 106-97-8)

PROPANE (CAS 74-98-6)

TWA	530 mg/m3

150 ppm

TWA	590 mg/m3

250 ppm

TWA	5 mg/m3	Respirable.

10 mg/m3	Total

STEL	545 mg/m3

125 ppm

TWA	435 mg/m3

100 ppm

TWA	1900 mg/m3

800 ppm

TWA	1800 mg/m3

## US. NIOSH: Pocket Guide to Chemical Hazards

Components

Type

Value

1000 ppm

## Form

SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7)

TALC (CAS 14807-96-6)

TWA	0.05 mg/m3	Respirable dust.

TWA	2 mg/m3	Respirable.

## US. Workplace Environmental Exposure Level (WEEL) Guides Components	Type

Value

PROPYLENE GLYCOL METHYL ETHER ACETATE (CAS 108-65-6)

## Biological limit values

ACGIH Biological Exposure Indices

TWA	50 ppm

| Components | Value | Determinant | Specimen | Sampling Time |
| --- | --- | --- | --- | --- |
| ACETONE (CAS 67-64-1) | 50 mg/l | Acetone | Urine | * |
| ETHYLBENZENE (CAS 100-41-4) | 0.15 g/g | Sum of mandelic acid | Creatinine in urine | * |
|  |  | and |  |  |
|  |  | phenylglyoxylic |  |  |
|  |  | acid |  |  |
| XYLENE (CAS 1330-20-7) | 1.5 g/g | Methylhippuric acids | Creatinine in urine | * |

* - For sampling details, please see the source document.

## Exposure guidelines

US - California OELs: Skin designation

PROPYLENE GLYCOL METHYL ETHER ACETATE (CAS 108-65-6)

Can be absorbed through the skin.

## Appropriate engineering controls

Good general ventilation (typically 10 air changes per hour) should be used. Ventilation rates should be matched to conditions. If applicable, use process enclosures, local exhaust ventilation,  or other engineering controls to maintain airborne levels below recommended exposure limits. If exposure limits have not been established, maintain airborne levels to an acceptable level. Provide eyewash station.

Individual protection measures, such as personal protective equipment    Eye/face protection	Wear safety glasses with side shields (or goggles).

## Skin protection

Hand protection	For prolonged or repeated skin contact use suitable protective gloves.

Other	Wear suitable protective clothing.

Respiratory protection	If permissible levels are exceeded use NIOSH mechanical filter / organic vapor cartridge or an air-supplied respirator.

Thermal hazards	Wear appropriate thermal protective clothing, when necessary.

## General hygiene considerations

When using do not smoke. Always observe good personal hygiene measures, such as washing after handling the material and before eating, drinking, and/or smoking. Routinely wash work clothing and protective equipment to remove contaminants.

# Physical and chemical properties

## Appearance

Physical state	Liquid.

Form	Aerosol. Liquefied gas.

Color	Not available.

Odor	Not available.

Odor threshold	Not available.

pH	Not available.

Melting point/freezing point	-305.68 °F (-187.6 °C) estimated

## Initial boiling point and boiling range

-43.78 °F (-42.1 °C) estimated

Flash point	-156.0 °F (-104.4 °C) estimated

Evaporation rate	Not available. Flammability (solid, gas)	Not applicable. Upper/lower flammability or explosive limits

## Flammability limit - lower

(%)

Flammability limit - upper (%)

1.9 %  estimated

12.8 %  estimated

Explosive limit - lower (%)	Not available.

Explosive limit - upper (%)	Not available.

Vapor pressure	2749.53 hPa estimated

Vapor density	Not available.

Relative density	Not available.

## Solubility(ies)

Solubility (water)	Not available.

## Partition coefficient (n-octanol/water)

Not available.

Auto-ignition temperature	550 °F (287.78 °C) estimated

Decomposition temperature	Not available.

Viscosity	Not available.

## Other information

Density	6.77 lbs/gal

Flammability class	Flammable IA estimated

## Heat of combustion (NFPA 30B)

25.26 kJ/g estimated

Percent volatile	74.44

Specific gravity	0.81

VOC	4.1124165 lbs/gal Regulatory 2.5686157 lbs/gal Material

492.776176 g/l Regulatory

307.788042 g/l Material

# Stability and reactivity

Reactivity	The product is stable and non-reactive under normal conditions of use, storage and transport.

Chemical stability	Material is stable under normal conditions.

## Possibility of hazardous reactions

Hazardous polymerization does not occur.

Conditions to avoid	Heat. Avoid temperatures exceeding the flash point. Contact with incompatible materials.

Incompatible materials	Strong acids. Acids. Strong oxidizing agents. Nitrates. Aluminum. Halogens. Phosphorus. Fluorine.

Chlorine.

## Hazardous decomposition products

No hazardous decomposition products are known.

# Toxicological information

## Information on likely routes of exposure

Inhalation	May cause damage to organs through prolonged or repeated exposure by inhalation. May cause drowsiness and dizziness. Headache. Nausea, vomiting. Prolonged inhalation may be harmful.

Skin contact	No adverse effects due to skin contact are expected.

Eye contact	Causes serious eye irritation.

Ingestion	Expected to be a low ingestion hazard.

## Symptoms related to the physical, chemical and toxicological characteristics

Headache. May cause drowsiness and dizziness. Nausea, vomiting. Severe eye irritation. Symptoms may include stinging, tearing, redness, swelling, and blurred vision.

## Information on toxicological effects

Acute toxicity	Narcotic effects.

## Components	 Species

2-PENTANONE (CAS 107-87-9)

## Acute Oral

Test Results

LD50	Rat	3.73 g/kg

ACETONE (CAS 67-64-1)

| Acute Dermal |  |
| --- | --- |
| LD50 | Rabbit | > 15800 mg/kg |
| Inhalation LC50 | Rat | 76 mg/l, 4 Hours |
| Oral LD50 | Mouse | 3000 mg/kg |
|  | Rat | 5800 mg/kg |

ETHYLBENZENE (CAS 100-41-4)

| Acute |  |
| --- | --- |
| Dermal LD50 | Rabbit | 17800 mg/kg |
| Oral |  |  |
| LD50 | Rat | 3500 mg/kg |

N-BUTANE (CAS 106-97-8)

## Acute Inhalation

LC50	Mouse	680 mg/l, 2 Hours

Rat	658 mg/l, 4 Hours

PROPANE (CAS 74-98-6)

## Acute Inhalation

LC50	Rat	> 1442.847 mg/l, 15 Minutes

XYLENE (CAS 1330-20-7)

| Acute Dermal |  |
| --- | --- |
| LD50 | Rabbit | > 43 g/kg |
| Inhalation LC50 | Mouse | 3907 mg/l, 6 Hours |
|  | Rat | 6350 mg/l, 4 Hours |
| Oral LD50 | Mouse | 1590 mg/kg |
|  | Rat | 3523 - 8600 mg/kg |

* Estimates for product may be based on additional component data not shown.

Skin corrosion/irritation	Prolonged skin contact may cause temporary irritation.

## Serious eye damage/eye irritation

Respiratory or skin sensitization

Causes serious eye irritation.

Respiratory sensitization	Not a respiratory sensitizer.

Skin sensitization	This product is not expected to cause skin sensitization.

Germ cell mutagenicity	No data available to indicate product or any components present at greater than 0.1% are mutagenic or genotoxic.

Carcinogenicity	May cause cancer.

## IARC Monographs. Overall Evaluation of Carcinogenicity

ETHYLBENZENE (CAS 100-41-4)	2B Possibly carcinogenic to humans.

SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7)	1 Carcinogenic to humans. TITANIUM DIOXIDE (CAS 13463-67-7)	2B Possibly carcinogenic to humans.

XYLENE (CAS 1330-20-7)	3 Not classifiable as to carcinogenicity to humans.

## OSHA Specifically Regulated Substances (29 CFR 1910.1001-1050)

Not listed.

## US. National Toxicology Program (NTP) Report on Carcinogens

SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7)	Known To Be Human Carcinogen.

Reproductive toxicity	Components in this product have been shown to cause birth defects and reproductive disorders in laboratory animals. Suspected of damaging fertility or the unborn child.

## Specific target organ toxicity - single exposure

Specific target organ toxicity - repeated exposure

May cause drowsiness and dizziness.

Causes damage to organs through prolonged or repeated exposure.

Aspiration hazard	Not an aspiration hazard.

Chronic effects	Causes damage to organs through prolonged or repeated exposure. Prolonged inhalation may be harmful. Prolonged exposure may cause chronic effects.

# Ecological information

Ecotoxicity	Toxic to aquatic life. Harmful to aquatic life with long lasting effects.

## Components

2-PENTANONE (CAS 107-87-9)

## Aquatic

Species

Test Results

Fish

ACETONE (CAS 67-64-1)

Aquatic Crustacea Fish

LC50

EC50 LC50

Fathead minnow (Pimephales promelas)

Water flea (Daphnia magna)

Rainbow trout,donaldson trout (Oncorhynchus mykiss)

1190 - 1290 mg/l, 96 hours

21.6 - 23.9 mg/l, 48 hours 4740 - 6330 mg/l, 96 hours

BARIUM SULFATE (CAS 7727-43-7)

## Aquatic

Crustacea

EC50

Tubificid worm (Tubifex tubifex)

28.61 - 38.03 mg/l, 48 hours

ETHYLBENZENE (CAS 100-41-4)

## Aquatic

Crustacea Fish

EC50 LC50

Water flea (Daphnia magna)

Fathead minnow (Pimephales promelas)

1.37 - 4.4 mg/l, 48 hours

7.5 - 11 mg/l, 96 hours

TITANIUM DIOXIDE (CAS 13463-67-7)

## Aquatic

Crustacea Fish

XYLENE (CAS 1330-20-7)

## Aquatic

Fish

EC50 LC50

LC50

Water flea (Daphnia magna) Mummichog (Fundulus heteroclitus)

Bluegill (Lepomis macrochirus)

> 1000 mg/l, 48 hours

> 1000 mg/l, 96 hours

7.711 - 9.591 mg/l, 96 hours

* Estimates for product may be based on additional component data not shown.

Persistence and degradability	No data is available on the degradability of this product.

## Bioaccumulative potential

| Partition coefficient n-octanol / water (log Kow) |  |
| --- | --- |
| 2-PENTANONE | 0.91 |
| ACETONE | -0.24 |
| ETHYLBENZENE | 3.15 |
| N-BUTANE | 2.89 |
| PROPANE | 2.36 |
| XYLENE | 3.12 - 3.2 |

Mobility in soil	No data available.

Other adverse effects	No other adverse environmental effects (e.g. ozone depletion, photochemical ozone creation potential, endocrine disruption, global warming potential) are expected from this component.

# Disposal considerations

Disposal instructions	Collect and reclaim or dispose in sealed containers at licensed waste disposal site. Contents under pressure. Do not puncture, incinerate or crush. Do not allow this material to drain into sewers/water supplies. Do not contaminate ponds, waterways or ditches with chemical or used container. Dispose of contents/container in accordance with local/regional/national/international regulations.

Local disposal regulations	Dispose in accordance with all applicable regulations.

Hazardous waste code	The waste code should be assigned in discussion between the user, the producer and the waste disposal company.

## Waste from residues / unused products

Dispose of in accordance with local regulations. Empty containers or liners may retain some product residues. This material and its container must be disposed of in a safe manner (see: Disposal instructions).

Contaminated packaging	Since emptied containers may retain product residue, follow label warnings even after container is emptied. Empty containers should be taken to an approved waste handling site for recycling or disposal. Do not re-use empty containers.

# Transport information

## DOT

UN number

UN proper shipping name Transport hazard class(es)

Class Subsidiary risk

Packing group

UN1950

Aerosols, flammable, 2.1

Not available.

-

Not applicable.

Special precautions for user Read safety instructions, SDS and emergency procedures before handling.

## IATA

UN number

UN proper shipping name Transport hazard class(es)

Class Subsidiary risk

Packing group Environmental hazards

UN1950

Aerosols, flammable, 2.1

Not available.

-

Not applicable. No.

Special precautions for user Read safety instructions, SDS and emergency procedures before handling.

## Other information

IMDG

Passenger and cargo aircraft

Cargo aircraft only

Forbidden. Forbidden.

## UN number

UN proper shipping name Transport hazard class(es)

Class Subsidiary risk

Packing group Environmental hazards

Marine pollutant EmS

UN1950

Aerosols, flammable, 2.1

Not available.

-

Not applicable.

No.

Not available.

Special precautions for user Read safety instructions, SDS and emergency procedures before handling.

## Transport in bulk according to Annex II of MARPOL 73/78 and the IBC Code

- Regulatory information

Not established.

US federal regulations	This product is a "Hazardous Chemical" as defined by the OSHA Hazard Communication Standard, 29 CFR 1910.1200.

All components are on the U.S. EPA TSCA Inventory List.

## TSCA Section 12(b) Export Notification (40 CFR 707, Subpt. D)

Not regulated.

## CERCLA Hazardous Substance List (40 CFR 302.4)

2-PENTANONE (CAS 107-87-9)	Listed.

ACETONE (CAS 67-64-1)	Listed.

BARIUM SULFATE (CAS 7727-43-7)	Listed.

ETHYLBENZENE (CAS 100-41-4)	Listed.

N-BUTANE (CAS 106-97-8)	Listed.

PROPANE (CAS 74-98-6)	Listed.

XYLENE (CAS 1330-20-7)	Listed.

## SARA 304 Emergency release notification

Not regulated.

## OSHA Specifically Regulated Substances (29 CFR 1910.1001-1050)

Not listed.

Superfund Amendments and Reauthorization Act of 1986 (SARA) Hazard categories	Immediate Hazard - Yes

Delayed Hazard - Yes

Fire Hazard - Yes Pressure Hazard - No Reactivity Hazard - No

## SARA 302 Extremely hazardous substance

Not listed.

## SARA 311/312 Hazardous	No

chemical

SARA 313 (TRI reporting)

Chemical name	CAS number	% by wt.

XYLENE	1330-20-7	1 to <5

ETHYLBENZENE	100-41-4	0.1 to <1

## Other federal regulations

Clean Air Act (CAA) Section 112 Hazardous Air Pollutants (HAPs) List

ETHYLBENZENE (CAS 100-41-4)

XYLENE (CAS 1330-20-7)

## Clean Air Act (CAA) Section 112(r) Accidental Release Prevention (40 CFR 68.130)

N-BUTANE (CAS 106-97-8)

PROPANE (CAS 74-98-6)

## Safe Drinking Water Act (SDWA)

Not regulated.

## Drug Enforcement Administration (DEA). List 2, Essential Chemicals (21 CFR 1310.02(b) and 1310.04(f)(2) and Chemical Code Number

ACETONE (CAS 67-64-1)	6532

## Drug Enforcement Administration (DEA). List 1 & 2 Exempt Chemical Mixtures (21 CFR 1310.12(c))

ACETONE (CAS 67-64-1)	35 %WV

## DEA Exempt Chemical Mixtures Code Number

ACETONE (CAS 67-64-1)	6532

## US state regulations

US. California Controlled Substances. CA Department of Justice (California Health and Safety Code Section 11100)

Not listed.

## US. California. Candidate Chemicals List. Safer Consumer Products Regulations (Cal. Code Regs, tit. 22, 69502.3, subd. (a))

ACETONE (CAS 67-64-1)

ETHYLBENZENE (CAS 100-41-4)

N-BUTANE (CAS 106-97-8)

SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7) TALC (CAS 14807-96-6)

TITANIUM DIOXIDE (CAS 13463-67-7) XYLENE (CAS 1330-20-7)

## US. Massachusetts RTK - Substance List

2-PENTANONE (CAS 107-87-9)

ACETONE (CAS 67-64-1)

BARIUM SULFATE (CAS 7727-43-7) ETHYLBENZENE (CAS 100-41-4)

N-BUTANE (CAS 106-97-8)

PROPANE (CAS 74-98-6)

SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7) TALC (CAS 14807-96-6)

TITANIUM DIOXIDE (CAS 13463-67-7) XYLENE (CAS 1330-20-7)

## US. New Jersey Worker and Community Right-to-Know Act

2-PENTANONE (CAS 107-87-9)

ACETONE (CAS 67-64-1)

BARIUM SULFATE (CAS 7727-43-7) ETHYLBENZENE (CAS 100-41-4)

N-BUTANE (CAS 106-97-8)

PROPANE (CAS 74-98-6)

SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7) TALC (CAS 14807-96-6)

TITANIUM DIOXIDE (CAS 13463-67-7) XYLENE (CAS 1330-20-7)

## US. Pennsylvania Worker and Community Right-to-Know Law

2-PENTANONE (CAS 107-87-9)

ACETONE (CAS 67-64-1)

BARIUM SULFATE (CAS 7727-43-7) ETHYLBENZENE (CAS 100-41-4)

N-BUTANE (CAS 106-97-8)

PROPANE (CAS 74-98-6)

SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7) TALC (CAS 14807-96-6)

TITANIUM DIOXIDE (CAS 13463-67-7) XYLENE (CAS 1330-20-7)

## US. Rhode Island RTK

ACETONE (CAS 67-64-1)

ETHYLBENZENE (CAS 100-41-4)

N-BUTANE (CAS 106-97-8)

PROPANE (CAS 74-98-6)

XYLENE (CAS 1330-20-7)

## US. California Proposition 65

WARNING: This product contains a chemical known to the State of California to cause cancer.

## US - California Proposition 65 - CRT: Listed date/Carcinogenic substance

ETHYLBENZENE (CAS 100-41-4)	Listed: June 11, 2004

SILICA, CRYSTALLINE QUARTZ (CAS 14808-60-7)  Listed: October 1, 1988

TITANIUM DIOXIDE (CAS 13463-67-7)	Listed: September 2, 2011

## International Inventories

Country(s) or region	Inventory name

Australia	Australian Inventory of Chemical Substances (AICS)

Canada	Domestic Substances List (DSL)

Canada	Non-Domestic Substances List (NDSL)

China	Inventory of Existing Chemical Substances in China (IECSC)

Europe	European Inventory of Existing Commercial Chemical Substances (EINECS)

Europe	European List of Notified Chemical Substances (ELINCS)

Japan	Inventory of Existing and New Chemical Substances (ENCS)

Korea	Existing Chemicals List (ECL)

New Zealand	New Zealand Inventory

Philippines	Philippine Inventory of Chemicals and Chemical Substances (PICCS)

United States & Puerto Rico	Toxic Substances Control Act (TSCA) Inventory

## On inventory (yes/no)*

No Yes No No No

No No No No No

Yes

*A "Yes" indicates that all components of this product comply with the inventory requirements administered by the governing country(s)

A "No" indicates that one or more components of the product are not listed or exempt from listing on the inventory administered by the governing country(s).

# Other information, including date of preparation or last revision

Issue date	6th March, 2018

Version #	01

HMIS® ratings	Health: 2* Flammability: 4

Physical hazard: 0

NFPA ratings	Health: 2 Flammability: 4

Instability: 0

Disclaimer	The information in the sheet was written based on the best knowledge and experience currently available. THE INFORMATION CONTAINED HEREIN IS BASED ON DATA BELIEVED TO BE RELIABLE AND THE MANUFACTURER DISCLAIMS ANY LIABILITY INCURRED FROM THE USE OR RELIANCE UPON THE SAME. THE INFORMATION GIVEN IS DESIGNED ONLY AS A GUIDANCE FOR SAFE HANDLING, USE, PROCESSING, STORAGE, TRANSPORTATION, DISPOSAL AND RELEASE AND IS NOT TO BE CONSIDERED A WARRANTY OR QUALITY

SPECIFICATION. The information relates only to the specific material designated and may not be valid for such material used in combination with any other materials or in any process, unless specified in the text. This safety information is not a license to use this material as claimed by any patents of third parties. The user alone must finally determine whether a contemplated use of this material will infringe any such patents, and for obtaining any required licenses.